## Slide 1: INDR 100 INTRODUCTION TO INDUSTRIAL ENGINEERING
Lecture #16
Linear Programming
Ceyda Oğuz
coguz@ku.edu.tr
Koç University

## Slide 2: Agenda of the Day
How to Build a Good Model?
Mathematical Programming Model Types
Graphical Representation
Analysis of Solutions
Notes: Class Exercise: Filsiz Boya Company
Bir önceki derste anlattım, buradan çıkarttım

## Slide 3: How to Build a Good Model?
Main considerations in building a model:
ease of understanding the model
ease of detecting errors in the model
ease of computing the solution
units of measurement, scaling the coefficients, robustness

## Slide 4: How to Build a Good Model?
Ease of understanding the model:
  use mnemonic (related) names for variables and constraints
Ease of detecting errors in the model:
  avoid formulation errors
    unbounded or infeasible models are usually indicators of error
    examine if a known solution is feasible
    examine if the optimal solution makes sense
    include sensible bounds on decision variables
Notes: Nimonik (hatırlatıcı, things that help us to remember)

## Slide 5: How to Build a Good Model?
Ease of computing the solution:
  realistic assumptions may simplify the model
  some procedures may detect redundancies and fix some variables to reduce the problem size
  some models have a special structure, which can be exploited to solve these models easily, e.g., assignment problem, transportation problem
  some models can be decomposed into smaller models
Units of measurement:
  make sure that left-hand-side and right-hand-side of the constraints have the same units
  disparity in the sizes of coefficients leads to unstable models
Notes: Units of measurement: scale variables da vardı ama ne demek olduğunu anlamadığım için kaldırdım

## Slide 6: Mathematical Programming Model Types
Mathematical Programming models are categorized in 3 main groups according to the nature of the decision variables and type of objective function and constraints:
    Linear Programming (LP)
    Nonlinear Programming (NLP)
    Integer Programming (IP)
Pure integer Programming (IP)
Mixed-integer Linear Programming (MILP)
Mixed-integer Nonlinear Programming (MINLP)
Mathematical Programming models can also be considered in two different classes according to the parameters involved:
    Deterministic Models:
      all of the problem data is known and fixed
    Stochastic Models:
      some or all of the variables in the problem can have random values

## Slide 7: Mathematical Model: Linear Programming
A Linear Programming (LP) model aims to maximize or minimize a linear function, subject to a set of linear constraints.
Hence an LP model consists of:
  A set of decision variables.
  A linear objective function.
  A set of linear constraints.

## Slide 8: Linear Programming
All variables have power of 1
All variables are either added or subtracted (not divided or multiplied)
The constraints must be of the following forms:
  , or
  =
The objective must be either maximization or minimization.

## Slide 9: Linear Programming Models
The most popular mathematical programming models are Linear Programming models and can be represented with two different notations:
Matrix Notation:
Algebraic Notation:

## Slide 10: Linear Programming Example: Automotive Manufacturing Plant
Algebraic Notation:
Matrix Notation:

## Slide 11: Linear Programming Models
Basic assumptions in Linear Programming models:
    Proportionality: contribution of each variable to the objective function and constraints is proportional to their level
    Additivity: the objective function and the constraints is the sum of the individual contributions of the activities that are represented by decision variables
    Divisibility: decision variables are allowed to have any values (real values) that satisfy the constraints
    Certainty: the data used in the model are known

## Slide 12: Nonlinear Programming Models
Nonlinear Programming models can be expressed as:
Basic characteristics of Nonlinear Programming models:
    Proportionality and/or Additivity conditions are not necessarily valid
    Divisibility: decision variables are allowed to have any values (real values) that satisfy the constraints
    Certainty: the data used in the model are known and constant
Example: Portfolio Optimization Problem

## Slide 13: Integer Linear Programming Models
In general, Integer Programming models can be expressed as:
Basic characteristics of Integer Programming models:
    Proportionality: contribution of each variable to the objective function and constraints is proportional to their level
    Additivity: the objective function and the constraints is the sum of the individual contributions of the activities that are represented by decision variables
    Divisibility: some or all of the decision variables are allowed to have only integer values (e.g., binary (0 or 1) or integer (0,1,2,...,n) that satisfy the constraints
    Certainty: the data used in the model are known
Example: Assignment Problem

## Slide 14: Basic Forms of Integer Programming Models
    Pure Integer Programming Models (IP):
    Mixed-integer Linear Programming Models (MILP):
    Mixed-integer Nonlinear Programming Models (MINLP):

## Slide 15: Example: Automotive Manufacturing Plant
Process Flow Diagram:
Problem Data:
Vehicle
Body
Paint
Shop
Painted Vehicle
Assembly
Shop
Finished Vehicle
Shop
Processing Time (min/unit)
Available Time
(min/day)
Truck
Car
Paint 6 10 480
8
480
Assembly
8
Profit
(TL/unit)
3000
2000
The marketing division reports that it would be impossible to sell more than 40 trucks a day.

## Slide 16: Example: Decision Variables
Decision Variables :
: number of trucks produced per day [unit/day]
: number of cars produced per day [unit/day]
The complete mathematical model for the Automotive Manufacturing Plant:
Subject to
Constraint 1
Constraint 2
Constraint 3
Nonnegativity constraint

## Slide 17: Graphical Representation
What can be shown?
The objective function and the constraints of the model, and
Solutions to the problem through the model

## Slide 18: Graphical Representation of the Problem
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
Constraint 1
Constraint 1
Write the constraint as an equality:
Plot the line
Identify the direction of the constraint

## Slide 19: Graphical Representation of the Problem
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
Constraint 1
Constraint 2
Constraint 2
Write the constraint as an equality:
Plot the line
Identify the direction of the constraint

## Slide 20: Graphical Representation of the Problem
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
Constraint 1
Constraint 2
Constraint 3
Constraint 3
Write the constraint as an equality:
Plot the line
Identify the direction of the constraint

## Slide 21: Graphical Representation of the Problem
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
Constraint 1
Constraint 2
Constraint 3
Nonnegativity constraints
Write the constraints as an equality
Plot the lines
Identify the direction of the constraint

## Slide 22: Graphical Representation of the Problem
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
Constraint 1
Constraint 2
Constraint 3
Feasible region
The set of all points
that satisfy all the
constraints of the
model is called a

## Slide 23: Solution of Problems
Solution: A solution to a mathematical model is obtained by specifying certain values for decision variables.
    Example: x1 = 0, x2 = 0 is a solution
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
Graphical Representation of the Automative Manufacturing Plant Problem:
Constraint 1
Constraint 2
Constraint 3
Feasible region

## Slide 24: Analysis of Solutions
Solution: A solution to a mathematical problem is obtained by
specifying certain values for decision variables. Solutions are
categorized as follows:
  Infeasible Solutions: If a solution does not satisfy at least one of the constraints, then the solution is infeasible.
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
  Ex: = 80, = 0
Constraints 2 and 3 are not satisfied.
Infeasible
Feasible

## Slide 25: Analysis of Solutions
Solution: A solution to a mathematical problem is obtained by
specifying certain values for decision variables. Solutions are
categorized as follows:
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
Feasible Solutions: If a solution satisfies all of the constraints, then the solution is feasible.
Ex: = 0, = 0
or
= 30, = 30

## Slide 26: Analysis of Solutions
Solution: A solution to a mathematical problem can be idenfied by the points in the feasible region as follows:
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
Interior Points
Boundary Points
Extreme Points
An extreme point (vertex) is the intersection of constraints that lies at the boundary of the feasible region.

## Slide 27: Analysis of Solutions
Solution: A solution to a mathematical problem is obtained by
specifying certain values for decision variables. Solutions are
categorized as follows:
Optimal Solution(s): If a solution gives the best objective function value while satisfying all of the constraints, then the solution is optimal.
Ex: = 40, = 20 is the optimal solution
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80

## Slide 28: Analysis of Solutions
Solution: A solution to a mathematical problem is obtained by
specifying certain values for decision variables. Solutions are
categorized as follows:
Unbounded Solution(s): If a solution can be made infinitely large without violating any of the constraints in the problem, then the solution is unbounded.
x
2
x1
10
20
30
40
10 20 30 40 50 60 70
50 60 70 80
Constraint 1
Constraint 2
Constraint 3